## Slide 1: Status of the Texas Petawatt laser and Experiments
Presented at the ICUIL 2010, Watkins Glen, NY
Texas Center for High Intensity Laser Science
The University of Texas at Austin
Erhard Gaul
University of Texas
Mikael Martinez
Ted Borger
Gilliss Dyer
Doug Hammond
Srdjan Marijanovic
Marty Ringuette
Ramiro Escamilla
Franki Aymond
Woosuk Bang
Joel Blakeney
Todd Ditmire
Texas Center for
High Intensity Laser Science
Petawatt laser
Capacitor room
Compressor

## Slide 2: Optical Parametric Amplification and mixed glass amplification produces a new type of Petawatt laser
Stretcher
Mode-locked
oscillator
Compressor
broadband
OPCPA
stages
100 fs, (16 nm), 2 nJ
mixed
glass
stages
Gain factor: 1010 energy gain: 1J
Gain factor: 400 energy gain: 250J
Gain narrowed
spectrum
35 nm
11 nm
200 J, 150 fs
1.3 PW
Goal: > 1 Petawatt

## Slide 3: The Texas Petawatt laser uses three OPCPA and two Nd:glass amplifier stages
FR
ISO
Rod
Disk Amp
BBO
YCOB
BBO
ISO
ISO
FR
Image inv.
oscillator
Pump 4J
Pump 4J
RGD lens
Roof top
FP
PC

## Slide 4: Two pump lasers were used to allow for separate timing between OPCPA stages II and III
OPCPA
Stage I
OPCPA
Stage II
200 mJ
0.8 J
OPCPA
Stage III
4.0 J
4J custom YAG laser

## Slide 5: An 8-pass, 64 mm, silicate Nd:glass rod amplifier brings the energy up to 20 J
Rod
FR
Radial Group Delay lens
up to 27 J achieved,
15-18 J goal for compression and low B-integral
Deformable mirror

## Slide 6: The final amplifier use two Nova amplifiers with phosphate Nd:glass disks
Disk Amp
ISO
up to 248 J achieved, with 80% charge voltage
Energy limited by gratings, not by gain.
14.7 nm

## Slide 7: The compressor is inside a 6x14 ft Aluminum vacuum chamber

## Slide 8: The Compressor has 85% efficiency with MLD (Multi Layer Dielectric) Gratings from LLNL
Footprints of beam of both passes overlap partially for efficient use of gratings (405x805 mm2 at 1740 l/mm)
l = 1050,1057,1064nm
1.02
1.03
1.04
1.05
1.06
1.07
1.08
1.09
0
0.2
0.4
0.6
0.8
1
Compressor transmission
wavelength [
m
m]
Grating distance =128 cm;1740 lines/mm

## Slide 9: After some time under vacuum the tip and roll parallelism would drift to the point that focusing was affected
> 24 hours after compressor pump down
Rotation parallelism only fixed
Rotation, tip, and roll fixed under vacuum
Focal spot (false color)
Roll
Tip
Rotation
• High bandwidth + high lines per mm
• Large heavy gratings
• Occurs despite breadboard being isolated from chamber down to feet

## Slide 10: Grating parallelism has low tolerance but is very important for pulse compression in space and time
[units: arc sec] | Rotat | Tip | Roll
Requirement (for <1 fs error) | 1 | 5 | 10
detection | ~1 | ~3 | ~3
achieved | 1-3 | ~3 | ~3
Step size resolution | 0.05 | .8 | .3
Reproducibility | ~.3 | 2 | 2
G1
G2
Rotation/Tip alignment (multipass with farfield)
Roll/Rotation alignment (multipass of Littrow)
Reference mirrors
Components used to solve issue
• High load motors replaced manual tip/roll
• Reference mirrors
• Two in-vacuum video cameras
• Two fiber lasers

## Slide 11: We tracked and eliminated major sources of pointing jitter to achieve RMS pointing stability < 7 µrad
7 µrad RMS horiz
5 µrad RMS vert
Current pointing jitter at target
Sources eliminated
• Laser enclosure vs. wind currents
• Mechanical pump isolation
• Improving rigidity of some supports
• Vibration resonances (ongoing)
µrad
2,3) Rod Amplifier midpoint and output
1) OPA output
4,5) Compressor input and output
7) Target
6) Focusing optic
Used far-field diagnostics at 7 locations

## Slide 12: Radial group delay of pulse front caused by large lenses must be corrected
Phase front: vphase = c/n
Pulse front: vgroup = c/(n-l dn/dl )
Phase front is flat for proper imaged system
Pulse front needs correction (f1(x,y)=const)
Pulse broadening of 5th order super-Gauss with ~70% fill factor
Solution requires:
(l dn/dl)system = 0
We have a negative lens/ aspheric mirror to correct this problem and built an special autocorrelator to measure Radial group delay
Problem:

## Slide 13: Radial shearing, 2nd order autocorrelation resolves radial group delay across the entire aperture
Upcollimating Telescope
Doubling
Crystal
Beam Splitter
CCD Camera
Imaging
Filters
Full down-collimated beam input
Mixed Signal
Expanded Beam
(locally flat)
Beam Overlap in Crystal
Small Beam (fits on CCD)
Crystal
Full “bowl”
Expanded, locally flat
CCD Camera
Beam Splitter
2ω Crystal
Intersection
An ordinary autocorrelator conceals RGD effects!

## Slide 14: Common autocorrelation techniques do not measure the effects of radial group delay
Up-collimating Telescope
Doubling
Crystal
Input
Imaging CCD detector
Doubling
Crystal
Input
Imaging CCD detector
3.6ps
24cm
3.6ps
24cm
1.1ps
220fs
120fs FWHM
150fs FWHM
Standard SHG autocorrelation will measure a narrow temporal overlap across the beam.
SHG correlation between the (full size) pulse and expanded center reference will measure relative temporal delay between beam center and edge.
False pulse duration
Problem typically arises in >20 TW TiSa lasers and > 100 TW glass lasers or fs microscopy (Bor J.M.Opt. 88), but is sometimes ignored due to incorrect measurement

## Slide 15: Radial group delay of pulse front can be corrected with achromatic system optics
Negative Lens
Aspheric
Mirror
Faraday Rotator
The Texas Petawatt 64 mm Rod Amplifier
Input from OPA
Retro
Output
Relay Telescope
Injection Relay Telescope
Rod Amp
corrector lens assembly
RGD correction installed in rod amplifier is optimized for all TPW telescopes

## Slide 16: Bulk optics radial group delay correction removes 1.1 ps of spatio-temporal delay
3.6ps
24cm
1.1ps
220fs
120fs FWHM
Calculated Radial Group Delay
Uncorrected -> 1.3 ps
Calculated Radial Group Delay
Corrected -> 13 fs
Uncorrected Radial Group Delay
Radius (a.u.)
Radius (a.u.)
Time (fs)
Time (fs)
Radius (a.u.)
Radius (a.u.)
Time (fs)
Time (fs)
24 cm
2.9 ps
< 150fs FWHM
Corrected Radial Group Delay
Simulation
Measurement

## Slide 17: We have installed a deformable mirror to remove and pre-correct measured wavefront distortion
• Wavefront sensor purchased in advance and used throughout system
• Deformable mirror can correct multiple waves of distortion (32 actuators)
• Rod and main amp shots induce thermal distortion
• The deformable mirror is placed at the mid point of the rod amplifier
The deformable mirror
wavefront sensor control
Location for deformable mirror

## Slide 18: Pre correction with several iterations are can correct the focus spot but add aberrations abfront
End Chain FF
Comp Input FF
OPA uncorrected
OPA corrected
Rod shot corrected
Rod shot add ~0.75 wave focus during shot

## Slide 19: A high f/# beamline enables a variety of experiments more suitable for soft focusing
Leak-through diagnostics
f/40 spherical mirror
Future f/22 focusing option
Full aperture beam pickoff diagnostic
Target chamber at focus
Beam dump
Cluster fusion setup
Compressor
Laser bay

## Slide 20: The radial group delay correction enabled the cluster fusion experiment to work properly

## Slide 21: Side image of gas jet shows increasing brightness of the plasma ~3mm below the nozzle
OPA shot 100 mJ
ROD amp shot 10 J
+ OD 2 filter
System shot 188 J
+ OD 3.6 filter
Laser input
Gas nozzle edge

## Slide 22
The first series of target shots on CD4 clusters reached peak powers above 1.3 Petawatt
FWHM = 130 fs
(130-160fs typical)
Chart: Energy on target [Joule]
End chain near field image has 65% fill factor
Focal spot has up to 25% Strehl ratio
22cm
diameter
Rod amp shots
System shots up to 189.5 J

## Slide 23: A F#/3 focus target chamber will be added by 12/2010
Laser bay
Compressor
F/40 focusing target system
Target chamber
F/3 focusing target system
Target bay
chamber
Diamond-turned parabola

## Slide 24: Alternate silicate glasses improve mixed glass bandwidth
Alternative silicate has broader spectrum and larger separation form phosphate fluorescence peak than standard silicate glass
Key properties are reasonable:
cross section (~70%)
n2 ( x 1.5-2 )
Lifetime long enough
Good thermal prop.
Good mechanical prop.
Good optical properties
S. E.Stokowski, et. al, LLNL-M-95,
Laser Glass Handbook 1981
New glass sample made and tested
Work in progress with SCHOTT for further broad bandwidth glass improvements and manufacturing of mid size rods

## Slide 25: Large gain in mixed glass can sustain bandwidth for <100 fs pulse duration
100fs/ 16nm is commercially available
Saturated beam (30 nm super Gaussian
Shaped spectrum
Sub 120 fs with gain ~ 107 !
Pulse duration for various mixed glasses and seed spectrum shaping
K824 /phosphate mix with modest shaping
Choice for basic seed spectrum shaping

## Slide 26: Nd:Glass petawatt lasers have the potential for scalability to multi petawatt lasers
NIF glass laser
Glass lasers have demonstrated above 26kJ energy in a single beam line
High bandwidth possible
Requires tiling (~3x5) of large gratings
10 PW class laser
2.2 KJ demonstrated at LLE
130 fs demonstrated at UT
Shorter pulses and higher bandwidth possible
1.5 m tiled gratings demonstrated
1.5 m single grating feasible
85 % compressor transmission demonstrated
100 PW class laser
LLE grating assembly

## Slide 27: The Glass Hybrid Optical Scaled Testbed (GHOST) laser provides lower energy and higher repetition rate
Mixed glass rod amplified:
  Pulsewidth: 115 fs
  Rate: 1 shot / minute
  Energy: 2 to 3 Joule
OPA only:
  80 fs pulses
  10 Hz / shot on demand
  8 mJ / pulse
Wavelength 1.054 µm
Interaction chamber
GHOST
10-7
100
Intensity
Delay (ps)
40
-80
0
Single shot 3rd order autocorrelation
Pulse contrast measurements

## Slide 28: The THOR laser, our original 30TW target shooter, is being upgraded to a petawatt (30J, 30 fs)
Thor Front End
Regen becomes OPA
Glass Laser
XUV Beamline
XUV Inter-action
PW Solid Target
Chamber
10 Hz Solid Target Chamber
Compressor
Final Amp
Future layout
• OPCPA front end
• Additional 10 Hz pump
• New 10 cm Ti:Sapp
• 2x 70 J @ 532 pump
• New compressor
• New target chamber
• New HHG beamline
Petawatt laser
Radiation shield wall
Capacitor room
Control room
Compressor
Clean room
Target area

## Slide 29: Summary
Radial group delay is corrected
Wavefront errors are pre-corrected to a large extend. Strehl ratio up to 0.25 achieved on system shots
Pointing error on target are below 7mrad
We have performed a series of target shot on gas jet targets with over 1.3 PW laser pulses.